## Slide 1
TROLL RESEARCH STATION
Updated Project Proposals week 3
Group 1: Iris Claus, Daphne Kamsteeg, Ludovica Perone Pacifico, Chloé Phan, Marieke van Wijk
IAP Workshop
Q3 2026
Prof. Henriette Bier, Arwin Hidding, Lisa-Marie Mueller, Vera Laszlo
TROLL RESEARCH STATION
Midterm presentation 13/3
Group 1: Iris Claus, Daphne Kamsteeg, Ludovica Perone Pacifico, Chloé Phan, Marieke van Wijk
IAP Workshop
Q3 2026
Prof. Henriette Bier, Arwin Hidding, Lisa-Marie Mueller, Vera Laszlo

## Slide 2
01
RESEARCH | ACTIVITY MAPPING
Individual
peripheral zones
Collective
central zones
Both
1.5 m
0.8 m
1.5 m
1.5 m
2 m
2.5 m
1.6 m
1.6 m
1.4 m
Hygiene
7.00 - 8.00
2.5 m
Working
14.00 - 18.00
Relaxing / exercising
18.00 - 20.00
Dining
20.00 - 21.00
1 h
1 h
1 h
4 h
2 h
Relaxing
21.00 - 22.00
Sleeping
22.00 - 7.00
Working
9.00 - 13.00
Dining
8.00 - 9.00
Dining
13.00 - 14.00
2.5 m
2.5 m
4 h
1 h
9 h
1 h
Highest duration. Lowest frequency, hence must be folded away or reconfigured. At extremities to minimise daytime circulation interference.
Highest frequency, hence must be easily accessible.
Demands maximum clearance of floor area.
Legend
demand two configurations, one for collective and one for private fruition
1.5 m
0.8 m
1.5 m
3.7 m
1.4 m
1.5 m
0.8 m
1.6 m
1.6 m
1.4 m
+ Storage space
of personal items, clothing, working equipment.
Fixed. Compact, to maximise space clearance
at least two modules
06.00
12.00
18.00
00.00
Notes: Activity mapping in container + minimum dimensions for each activity.
lighting requirements for each activity? (is it a repetition with lighting needs?)

## Slide 3
ACTIVITY MAPPING | SCENARIO ANALYSIS
1 - Standard ops day
2 - Active recovery day
5 - Patient care
4 - Asynchronous shifts
3 - Emergency mode
Separate beds with integrated personal storage and privacy separator. For optimized circulation with no functional overlap and light and acoustic shielding in sleeping zone.
Adjustable modules for user-driven spatial reconfiguration to enable environmental personalization and reduce visual monotony.
Foldable partition to subdivide container into two private rooms. For increased privacy and psychological benefits during prolonged isolation
Foldable partition to subdivide container into two private rooms.. Indepentent light control between the two zones. For increase acoustic and light insulation.
Bed at ergonomic standing height and integrated bedside surface to enable assisted care.
02
Notes: update based on evolutio of design

## Slide 4
03
LECTURE SUMMARY | VORONOI
What is Voronoi?
  Mathematical Partitioning: Dividing space into cells based on proximity to "seed points."
  Nature’s Blueprint
  Organic Efficiency: eliminating "dead corners"
Application & Objective
  Optimal Spatial Efficiency
  Transforming "stiff" furniture into foldable furniture
  Breaking the Box: eliminates "tunnel vision"

## Slide 5
Kinetic skin
Static core
Distribution principles
Legend
More space-consuming and/or fixed furnitures are placed adjacent to the walls. For individual fruition
  Storage 2. Bed 3. Workstation
Furniture in the center of the container is easily reconfigurable and can be folded to a surface, for maximum clearance of the space. For both collective or individual fruition
4. Multipurpose room divider 5. Chair/Lounge chair 6. Table
04
ADAPTIVE FURNISHING | OVERVIEW
1
1
1
1
2
2
3
3
4
4
6
5
6
5

## Slide 6
05
KINETIC SKIN | GENERATION PROCESS
Voronoi points population on the wall plane
Checking how the generated cells look like
Manually re-arranging the Voronoi points to have horizontal demarcations for folds
Organization of the newly generated cells
Base Voronoi pattern
Re-arranged pattern

## Slide 7
05
KINETIC SKIN | GENERATION PROCESS
Selecting the cells for the seating and table
Unfolded seating and table

## Slide 8
Dining table and chairs open (for dining)
Just chairs open (for socialising)
06
KINETIC SKIN | CONFIGURATIONS
Collective
Everything closed (for collective excercising)
8.00h-9.00h, 13.00h-14.00h, 20.00h-21.00h
8.00h-9.00h, 13.00h-14.00h, 14.00-18.00 20.00h-21.00h
18.00h-20.00h

## Slide 9
Individual table + chair open (for individual dining)
Lounge chairs open (for resting)
06
Individual
Lounge chair + individual table open (for resting with side table next to it)
Chairs folded towards the center (for socialising while maintaining privacy inside the room)
8.00h-9.00h, 13.00h-14.00h, 20.00h-21.00h
18.00h-20.00h, 21.00-22.00
18.00h-20.00h, 21.00h-22.00h
9.00h-13.00h
KINETIC SKIN | CONFIGURATIONS

## Slide 10
Just wall (for individual excercising)
06
Individual
Lounge chair in individual configuration, dining in collective one
Hybrid
18.00h-20.00h
18.00h-20.00h
KINETIC SKIN | CONFIGURATIONS

## Slide 11
07
STATIC CORE | GENERATION PROCESS
Process
  Optimisation of activities distribution in space
minimal dimensions obtained from activity mapping
  Centroids as seeds points
minimal dimensions obtained from activity mapping
Optimised ergonomic design
Dining storage
Bed
Bedside table
Clothing storage
Work station
Work equipment storage
Bed safety barrier

## Slide 12
Waking up
Getting off the bed
08
ADAPTIVE FURNISHING | 24H MAPPING
6.00-7.00: Waking up & Hygine - User 1
Getting clothes from wardrobe
Closing wardrobe and bed safety barrier
Bed ladder integrated in clothing storage surface

## Slide 13
Waking up
Getting off the bed
ADAPTIVE FURNISHING | 24H MAPPING
7.00-8.00: Waking up & Hygine - User 2
Getting clothes from wardrobe
Closing wardrobe and bed safety barrier
08
Extended bed
(alternatively serving as additional storage)

## Slide 14
Getting food/dishes from kitchen storage
ADAPTIVE FURNISHING | 24H MAPPING
8.00-9.00: Individual Dining - User 2
Folding out dining chair and table
Having breakfast
08

## Slide 15
9.00-13.00: Individual Working - User 2
Working
Folding away bed
ADAPTIVE FURNISHING | 24H MAPPING
Working
Folding out desk and work bench
Folding in desk and work bench
08
Allows fruition of larger space in heigth, natural light and view of the sky from skylight above bed
allows fruition of window and storage

## Slide 16
ADAPTIVE FURNISHING | 24H MAPPING
13.00-14.00: Individual Dining - User 2
Putting food/dishes back in kitchen storage
Having lunch
08

## Slide 17
14.00-18.00: Collective Working
ADAPTIVE FURNISHING | 24H MAPPING
Working
Folding out table and chair
Reconfiguring walls
08

## Slide 18
18.00-20.00: Relaxing/Exercising
Reconfiguring walls
ADAPTIVE FURNISHING | 24H MAPPING
Relaxing/exercising
Folding out lounge chair
08
Notes: Hi I did that part (slides 27 to 29)
(do you want me to delete these or keep) ?
I also thought of doing the screen recordings for the table and chair part next to the diagrams on slides 27-29 to see the cells better, can I do it ?

## Slide 19
20.00-21.00: Collective dining
Reconfiguring walls
ADAPTIVE FURNISHING | 24H MAPPING
Folding away lounge chair
Folding out table and chairs
Dining
08
Notes: Hi I did that part (slides 27 to 29)
(do you want me to delete these or keep) ?
I also thought of doing the screen recordings for the table and chair part next to the diagrams on slides 27-29 to see the cells better, can I do it ?

## Slide 20
Relaxing
Reconfiguring wall
21.00-22.00: Relaxing
Folding in chair and table
ADAPTIVE FURNISHING | 24H MAPPING
08
Notes: Hi I did that part (slides 27 to 29)
(do you want me to delete these or keep) ?
I also thought of doing the screen recordings for the table and chair part next to the diagrams on slides 27-29 to see the cells better, can I do it ?

## Slide 21
Climbing up the bed
21.00-22.00: Relaxing & Sleeping - User 1
Folding out ladder and bed safety barrier
ADAPTIVE FURNISHING | 24H MAPPING
Sleeping
In bed activities
08
Notes: Hi I did that part (slides 27 to 29)
(do you want me to delete these or keep) ?
I also thought of doing the screen recordings for the table and chair part next to the diagrams on slides 27-29 to see the cells better, can I do it ?

## Slide 22
Sleeping
Climbing up the bed
ADAPTIVE FURNISHING | 24H MAPPING
22.00-23.00: Sleeping - User 2
Foldinf out ladder and bed safety barrier
08

## Slide 23
Primary
LIGHTING | NEEDS
Ambient lighting
Base lighting
Navigating lighting
Task lighting
Secondary
Secondary
Secondary
Tertiary
09
Natural light
Notes: With our activity mapping, we established our lighting needs, Which we divided Into primary secondary and tertiary.
The primary lighting need is the circadian light, which will be the base lighting.
Layered on top will be the Secondary lighting like, task-, ambient- and natural light. (Additional)
And last, Tertiary lighting, our navigation lighting. (Incidental)

## Slide 24
LIGHTING | ARCTIC AND CIRCADIAN
  Arctic winter: the sun never rises above the horizon-> no direct sunlight, dim light 1-50lux and very cool blue twilight
  Arctic summer: the sun never sets, moves circular in the sky --> low angle warm light, 5-20,000 and 20.000-100.000 lux
  Circadian cycle: Bright daytime light, dark nights and regular 24h cycles
10
Problem:
Arctic conditions provide either
  Too much light ⟶ Summer
  Too little light ⟶ Winter
Solution:
Permanent Circadian sleep/wake light cyle
  artificially managed
Is there any way to use the Arctic light?
Notes: So when looking at the arctic daylights and circadian rythm, we see a lot of diffeerences.
the problem: the natural arctic light cycle is either excessively bright or almost absent (winter).
Sollution
but iss there any way to use arctic liggt

## Slide 25
LIGHTING | ARCTIC AND CIRCADIAN
10
Arctic winter
Arctic summer
Windows are not a reliable primary light source in the Arctic environment
But provide essential phycophysiological benefits
Skylight window
Window eye level
For orientation:
  seeing the outside ⟶
improves wellbeing through visual connection
  make the space ‘feel’ wider & less isolated
  helps to stay connected to outside world
For light:
  gives a stronger ‘feeling’ of daylight
  help space feel less enclosed
  works well together with artificial circadian lighting
Notes: For oreintation:
helps people to see the horizon ⟶
improves wellbeing through visual connection
helps to stay connected to outside world
For light:
help space feel less enclosed
works well together with artificial circadian lighting

## Slide 26
LIGHTING | ARCTIC AND CIRCADIAN
10
Windows can support the circadian light cycle inside the container
but must be controlled to support the system
Arctic winter
Arctic summer
There is too much light from the window
  Solar-control glass, filters brightness
  Diffusion, softens glare
  Shading, blocks excess light (lux-sensors)
  Artificial night, shading blocks all natural light
  Artificial lighting dims to maintain circadian schedule inside with AI (lux- & CCT-sensors)
There is too little light from the window
  Circadian daylight cycle as primary light provider
  is about perception an information not light
  Artificial lighting adjusts color to maintain circadian schedule inside with AI ( CCT-sensors)
The AI system dynamically adjusts intensity and CCT in relation to outside to maintain the “controlled artificial day” despite changing external lighting conditions.
Notes: as mentioned before..

## Slide 27
1
LIGHTING OVERVIEW
11
1
1
1
2
2
3
3
4
4
1
1
Notes: overview of what activity has what location etc, linking activities to lighting to ai

## Slide 28
LIGHTING OVERVIEW
11
5
6
7
8
9
8
9
8
9
Notes: overview of what activity has what location etc, linking activities to lighting to ai

## Slide 29
LIGHTING | OPTIMAL LUX AND CCT
12
Secondary
Primary
Notes: Based on the activity mapping, we identified the optimal ranges for illuminance and colour per activity and time of the day

## Slide 30
Strategy
Minimising n. of different control systems, detection errors and maintenance requirements
3 systems
  Computer Vision (CV) → Acts as the 'eyes'.
  Smartwatch → Provides the 'biological data'.
  Manual Overrides → Users can always take control via manual sliders
Hierarchy
1. individual preferences and adaptation
2. environmental context
Health Safeguards
  Red Warning: Shown when manual settings are outside healthy ranges.
  Corrective Fade: A gradual 30-minute transition back to healthy light levels.
Dual Control Logic
We distinguish between Trigger Control (turning lights on/off) and Atmospheric Control (adjusting CCT and Lux).
13
LIGHTING AND AI |CONTROL SYSTEMS
Brightness
–
–
–
–
–
Light colour
–
–
–
–
–
W
C
Brightness
–
–
–
–
–
Light colour
–
–
–
–
–
W
C
Sliders for manual control
Sliders for manual control for values outside of safeguard limits
MANUAL OVERRIDERS
LIGHTS
COMPUTER VISION
AI SYSTEM
SMARTWATCH
ON/OFF
CCT/LUX

## Slide 31
Layer 1: Identity
  Key: smartwatch (who is in the room?)
  Personal preferences: CCT & Lux
  Circadian: sunrise simulation (30 min)
Layer 2: Activity
  Eyes: computer vision
  Intent: Detects when the desk is unfold to activate a 'Work' scene
  Stress-relief lighting (heart rate)
Layer 3: Context
  Exterior sync: actic weather data
  Polar night: increases the light quality to mimic sunlight (High CRI)
  Midnight sun: digital darkness (melatonin support)
15
LIGHTING AND AI |CONTROL SYSTEMS
Unfolded → light goes on
Folded → Light goes off

## Slide 32
16
Two Modes: Vision-Driven Logic
Computer Vision recognizes the furniture configuration to trigger the correct mode automatically.
  Collective Mode (Table Centered):
    Trigger: Table in the center (detected by CV).
    Collective Balancing. The AI calculates an average between both users.
    All lighting zones are synced to for example a warm 3000K setting for shared activities.
  Private Mode (Table Rotated or Split):
    Trigger: Table split or rotated.
    The AI divides the container into two personalized "light bubbles."
    These bubbles follow the residents through the space using UWB (Apple Watch) tracking.
LIGHTING AND AI | AMBIENT LIGTHTING
Collective mode
Private mode
transition zone

## Slide 33
TUTORIAL 27/02/26 OF JUPITER NOTEBOOK
The values the Jupiter Notebook model produces is the prediction of what the lux should be according to the model. This model uses the technique of neural networks.
Machine learning, unlike AI, infers patterns from data while AI needs the patterns as an input.
To implement the control systems we used machine learning to control
and predict the lighting systems, this was done by a Jupyter Notebook code with neural networks.
17
MACHINE LEARNING | INTRODUCTION

## Slide 34
SUPERVISED LEARNING
  FEATURES ARE THE INPUT VARIABLES, POSSIBLE FEATURES;
    Weather features; outdoor_temp, direct_normal_radiation, rel_humidity, diffuse_normal_radiation, global_horizontal_radiation, infrared_radiation, direct_normal_illumination, diffuse_horizontal_illumination, global_horizontal_illumination, total_sky_cover.
    Physological features; hrv_rmssd_ms, heart_rate_bpm, pupil_mm, blink_rate_per_min, skin_conductance_uS, respiratory_rate_bpm.
  LABELS ARE THE OUTPUT VALUES, IN THIS CASE THE PREDICTED ILLUMINANCE_LUX AND CCT_kelvin
SELECTING THE FEATURES AND LABELS: BALANCING ACCURACY OF MODEL WITH RISK OF OVERFITTING
  Choosing and grouping features.
    Features with high correlation >0.8 with each other may be redundant, so they can be grouped or dropped.
    Features with high correlation with labels are likely strong predictors.
  With cross-validation we are testing the overfitting, if results are similar to the test score, that means low overfitting.
18
MACHINE LEARNING | PRE-TRAINING
Feature correlation heatmap

## Slide 35
feature grouping
  For the weather features e.g. I found strong correlations, which can be grouped together to reduce redundancy: Direct radiation and direct illumination (0.94) and diffuse horizontal and global horizontal illumination (0.88)
  For the physiological features e.g. I found inversely correlated features, one of these can be used as a representative feature. HRV and heart rate (0.85).
EVALUATING MODEL PERFORMANCE
  R-square is used to evaluate how well the model represents the data (the variance of the mean). For example, if R-square is 80%, then the model can express 80% of the variability.
  Error functions such as RMSE and MAE provide information about how far off the estimation is from the actual value. RMSE penalizes large errors and MAE takes the average. Both of the scores are relative to the scale of the dataset.
  Performance of the first model vs second model trained with adjusted features;
  R-square = 0.13752631245104485 → 0.6972536094819399,
  RMSE = 547.2232257652937 → 401.7306132398937,
  MAE = 463.33269614523095 → 322.292021438062
  Conclusion; clear improvement of the model performance.
19
MACHINE LEARNING | TRAINING

## Slide 36
20
MACHINE LEARNING | TRAINING - FEATURE GROUPS

## Slide 37
21
MACHINE LEARNING | TRAINING - EXAMPLE
>90 bpm
Stressed
< 20 ms
200-350
lux
2700-3500 K
Calm/relaxed
60 - 90 bpm
20 - 70 ms
500-700
lux
4000-5000 K

## Slide 38
23
CHOOSEN FRAGMENT
A piece of the kinetic wall:
Lounge chair/DIning chair

## Slide 39
Thank you for your attention !