## Slide 1
TRANSITIONS
rone Pacifico, Chloé Phan, Marieke van Wijk
IAP Workshop - Q3 2026
Prof. Henriette Bier, Arwin Hidding, Lisa-Marie Mueller, Vera Laszlo
ITIONS
habitat for Troll research station
research station
Iris Claus, Daphne Kamsteeg, Ludovica Pe

## Slide 2
01
CONTENT
00
02
03
Introduction
Current situation & problem statement
Goal
Project principles
Design
Voronoi-based approach
Activity mapping
Design concept
References
Principles & process
Reconfiguration
24h cycle
Lighting & AI
Lighting layers
Circadian rythm
Natural lighting integration
Control systems - 3 layers
Control systems - Adaptive control
Machine learning
04
Systems integration
Configuration C1
Configuration C2
Configuration C3
Digital prototype
Lighting
Fragment logic
Structural optimisation
Material
05

## Slide 3
01
INTRODUCTION| CURRENT SITUATION & PROBLEM STATEMENT
Site of Troll research station (DigitalMuseum)
Habitation module interior (MAGIC-DML Team)
Living in a confined, monofunctional space, with natural and artificial lighting that fail to support circadian rhythms during the extreme shifts of the Midnight sun and Polar night
Arctic seasons Lighting needs Spatial limitation
Problem statement
Notes: Context: Users live and work in compact research stations (e.g., Troll Station, Antarctica)
Problem: Spatial, physiological, and psychological constraints
Opportunity: Need for flexible, adaptive design → leads to nature-inspired Voronoi logic
Challenges:
Limited or no natural light → impacts health, sleep, productivity
Small, static spaces → don’t adapt to activities or individual needs
Conflicting rhythms and preferences → affects wellbeing

## Slide 4
Midnight sun
(3-4 months)
Midnight sun
(3-4 months)
Polar night
(3-4 months)
Twilight period
(1-2 months)
Shoulder seasons
(1-2 months)
To create an efficient, reconfigurable and smart space that fulfills the psychological and physical needs of its inhabitants with 3 main principles
-
01
INTRODUCTION| GOAL
Goal
Daylight Chart for Norway’s Troll Antarctic Research Station (EP Salt)
Notes: change text & Also mention what we are designing for:
-2 people
-emergency situation, different schedules
-for most extreme conditionsduring the 8 month

## Slide 5
VORONOI | AI | LIGHTING
01
INTRODUCTION| PROJECT PRINCIPLES

## Slide 6
DESIGN

## Slide 7
  Equidistant vertices/edges
d
d
d
d
1
d
1
  Nearest neighbour
  Point vertical/
horizontal
alignment
  Point density variation
⟶ Center of activities as seed points
⟶ Lighting in edges
⟶ Function variation
⟶ Horizontal/
vertical
surfaces
02
Generation
Configurations
Properties
  Random seed points
  Delaunay triangulation
  Extending triangles bisectors: voronoi cells
2D
vs
3D
max space clearance
fast reconfiguration
temporary activities
ergonomic niches
permanent activities
alignment with geometry of the container
max storage efficiency
Irregular
vs
Orthogonal
DESIGN | VORONOI-BASED APPROACH
Notes: Activity mapping in container + minimum dimensions for each activity.
lighting requirements for each activity? (is it a repetition with lighting needs?)

## Slide 8
Individual
peripheral zones
Collective
central zones
Both
Legend
demand two configurations, one for collective and one for private fruition
1.5 m
0.8 m
1.5 m
1.5 m
2 m
2.5 m
1.6 m
1.6 m
1.4 m
Hygiene
7.00 - 8.00
2.5 m
Working
14.00 - 18.00
Relaxing / exercising
18.00 - 20.00
Dining
20.00 - 21.00
Relaxing
21.00 - 22.00
Sleeping
22.00 - 7.00
Working
9.00 - 13.00
Dining
8.00 - 9.00
Dining
13.00 - 14.00
2.5 m
2.5 m
4 h
1 h
06.00
12.00
18.00
00.00
Highest duration. Lowest frequency, hence must be folded away or reconfigured. At extremities to minimise daytime circulation interference.
Highest frequency, hence must be easily accessible.
Demands maximum clearance of floor area.
1.5 m
0.8 m
1.5 m
3.7 m
1.4 m
1.5 m
0.8 m
1.6 m
1.6 m
1.4 m
+ Storage space
of personal items, clothing, working equipment.
Fixed. Compact, to maximise space clearance
at least two modules
1 h
1 h
1 h
4 h
2 h
9 h
1 h
In time & space
In height
0.45 m
1.70 m
2.10 m
2.50 m
High intensity use
low/medium intensity use
“dead space”
02
DESIGN | ACTIVITY MAPPING
Notes: Activity mapping in container + minimum dimensions for each activity.
lighting requirements for each activity? (is it a repetition with lighting needs?)

## Slide 9
DESIGN | CONCEPT
TRANSITIONS
2D/foldable
3D/Reconfigurable
Collective
Private
02

## Slide 10
Scott Snibbe, 1998
Boundary Functions (Snibbe.com)
RAAAF, 2014
The End of Sitting (RAAAF.nl)
02
DESIGN | REFERENCES
Notes: Activity mapping in container + minimum dimensions for each activity.
lighting requirements for each activity? (is it a repetition with lighting needs?)

## Slide 11
0.6 m
1.0 m
1.0 m
0.6 m
0.45 m
0.45 m
0.35 m
0.35 m
  2. Width-based zoning
Transition 2d-3d
  Storage in corners
  3. Boundary reconfigurability
Transition orthogonal-voronoi
Transition collective-private
0.25 m
0.25 m
Shelves
Seating
Storage
Sleeping area/ workstation
02
DESIGN | PRINCIPLES & PROCESS
Notes: Activity mapping in container + minimum dimensions for each activity.
lighting requirements for each activity? (is it a repetition with lighting needs?)

## Slide 12
DESIGN | RECONFIGURATION
02

## Slide 13
DESIGN | 24H CYCLE
02
Notes: Activity mapping in container + minimum dimensions for each activity.
lighting requirements for each activity? (is it a repetition with lighting needs?)

## Slide 14
LIGHTING & AI

## Slide 15
Primary lighting
LIGHTING & AI | LIGHTING LAYERS
Secondary lighting
Tertiary lighting
Natural lighting
03

## Slide 16
Waking up
Working
Relaxing
Sleeping
CCT: 2700-4000 K
Illuminance: 100-300 lux
CCT: 5000-6000 K
Illuminance: 500-1000 lux
CCT: 2200-3000 K
Illuminance: 50-200 lux
CCT: 1800-2200 K
Illuminance: 0-50 lux
03
LIGHTING & AI | CIRCADIAN RYTHM
Notes: With our activity mapping, we established our lighting needs, Which we divided Into primary secondary and tertiary.
The primary lighting need is the circadian light, which will be the base lighting.
Layered on top will be the Secondary lighting like, task-, ambient- and natural light. (Additional)
And last, Tertiary lighting, our navigation lighting. (Incidental)
no times: so it functions for both schedules

## Slide 17
200–350 lux
artificial circadian contribution:
250–450 lux
CCT: 5500-6500 K
Illuminance: 750-1000 lux
5-20 lux
Midnight sun
Polar night
filtered window contribution
final perceived
artificial circadian contribution:
450–730 lux
filtered window contribution
03
LIGHTING & AI | NATURAL LIGHT INTEGRATION
Notes: With our activity mapping, we established our lighting needs, Which we divided Into primary secondary and tertiary.
The primary lighting need is the circadian light, which will be the base lighting.
Layered on top will be the Secondary lighting like, task-, ambient- and natural light. (Additional)
And last, Tertiary lighting, our navigation lighting. (Incidental)

## Slide 18
LIGHTING & AI | CONTROL SYSTEMS - 3 LAYERS
03
CONTEXT
LAYER 3
USER
LAYER 2
ACTIVITY
LAYER 1
Environment
Motion Sensors
Smartwatch
Decision
system
AI
CCT
&
INTENSITY
Input
Output
Color &
Intensity
On/Off

## Slide 19
–
–
–
–
–
–
–
–
–
–
LIGHTING & AI | CONTROL SYSTEMS - ADAPTIVE CONTROL
ON OFF
Illuminance
Illuminance/ CCT limits
Health issues
Color
1 USER
2 ACTIVITY
3 CONTEXT
Environment
Motion Sensors
Smartwatch
CCT
&
INTENSITY
Control System
Manual Overrides
Safety check
30 min corrective fade
03
Notes: Health Safeguards:
Red Warning: Shown when manual settings are outside healthy ranges.
Corrective Fade: A gradual 30-minute transition back to healthy light levels.

## Slide 20
Private configuration
Collective configuration
Semi private configuration
Cool light
Dark
Warm light
Legend
LIGHTING & AI | CONTROL SYSTEMS - ADAPTIVE CONTROL
Personal preferences
Transition zone
Balancing between both preferences
Personal preferences
Personal preferences
Balanced lighting
03
Personal preferences

## Slide 21
LIGHTING & AI | CONTROL SYSTEMS - ADAPTIVE CONTROL
30 min corrective fade
03
Cool light
Dark
Warm light
Legend
Balanced lighting
CCT: 5000-6000 K
Illuminance: 500-1000 lux
CCT: 2200-3000 K
Illuminance: 50-200 lux

## Slide 22
LIGHTING & AI | MACHINE LEARNING
03
Feature correlation heatmap
  Machine learning to transform the system from reactive
→ predictive
  Jupyter Notebook
  Supervised learning
  Neural networks
Notes: Supervised learning uses input variables, called features, to predict output values, called labels.
Possible weather features include temperature, humidity, radiation, illumination, and sky cover.
Possible physiological features include heart rate, HRV, pupil size, blink rate, skin conductance, and respiratory rate.
The output labels in this case are the predicted illuminance (lux) and CCT (Kelvin).
Feature selection is important because the model must balance accuracy with the risk of overfitting.
Features with very high correlation to each other may be redundant, so they can be grouped or removed.
Features with high correlation to the labels are likely to be strong predictors for the model.
Cross-validation is used to check overfitting, and if the validation results are close to the test score, the model is likely not overfitting strongly.

## Slide 23
  feature grouping based on correlation heatmap
LIGHTING & AI | MACHINE LEARNING
Data grouping
03
INPUT HIDDEN OUTPUT
Physological Features
Weather Features
HVR
heart rate
pupil dialationil
blink ratek
skin conductance
respiration rate
Illuminance LUX
CCT Kelvin
temperature
humidity
skycover
diffuse radiation
global horizontal radiation
infrared radiation
direct radiation
direct illumination
diffuse horizontal illuminatio
global horizontal illumination
1
2
3
4
5
6
7
Filtering out redundant features
  Features with a high positive correlation could be measuring the same thing, so removing them prevents the model from overfitting
  Scatter plots will show this correlation

## Slide 24
LIGHTING & AI | MACHINE LEARNING
Scatterplot Illuminance
03

## Slide 25
LIGHTING & AI | MACHINE LEARNING
Scatterplot CCT
03

## Slide 26
FINAL FEATURE GROUPS | WHAT DO THEY REPRESENT | TYPE OF CORRELATION
hrv_rmssd_ms + heart_rate_bpm | Stress level of person | High negative correlation
skin_conductance_uS + respiratory_rate_bpm + blink_rate_per_min | Stress, alertness, tiredness of person | High positive correlation
outdoor_temp + rel_humidity + total_sky_cover | Atmospheric conditions | Differs
global_horizontal_radiation + infrared_radiation + direct_normal_radiation + diffuse_horizontal_illumination | Scatterd light in atmosphere | Differs
  Redundant features were removed or grouped
  Direct normal illumination, global horizontal illumination, diffuse normal radiation and pupil size were dropped
LIGHTING & AI | MACHINE LEARNING
Data grouping conclusion
03

## Slide 27
INPUT HIDDEN OUTPUT
Physological Features
Weather Features
HVR
heart rate
skin conductance
respiration rate
blink rate
temperature
humidity
skycover
diffuse radiation
global horizontal radiation
infrared radiation
Illuminance
CCT Kelvin
1
2
3
4
LIGHTING & AI | MACHINE LEARNING
03
INPUT HIDDEN OUTPUT
Physological Features
Weather Features
HVR
heart rate
pupil dialationil
blink ratek
skin conductance
respiration rate
Illuminance LUX
CCT Kelvin
temperature
humidity
skycover
diffuse radiation
global horizontal radiation
infrared radiation
direct radiation
direct illumination
diffuse horizontal illuminatio
global horizontal illumination
1
2
3
4
5
6
7
Data grouping before & after dropped features

## Slide 28
  The model was trained with the first selected features and compared to the final feature groups
  The model performance was evaluated using R², RMSE, and MAE
  The results show a strong improvement in accuracy, with higher R² and lower error values
CCT
  R-square = 27,5% → 80,2%
  RMSE = 761.90 → 397.62
  MAE = 321.18 → 239.49
Illuminance
  R-square = 75,4% → 96,1%
  RMSE = 292.06 → 116.67
  MAE = 239.49 → 93.74
LIGHTING & AI | MACHINE LEARNING
Training and evaluating model
03
Notes: TRaining the model
The model was trained with the selected features. To see if this selection made an positive impact, the performance of the first model was compared to the second model trained with adjusted features.
Evaluating model performance
R-square is used to evaluate how well the model represents the data in %.
Error functions such as RMSE and MAE provide information about how far off the estimation is from the actual value. RMSE penalizes large errors and MAE takes the average. Both are relative to the scale of the dataset.
Illuminance
R-square = 75,4% → 96,1%
RMSE = 292.06 → 116.67
MAE = 239.49 → 93.74
Conclusion: clear improvement of the model performance.

## Slide 29
SYSTEMS INTEGRATION | CONFIGURATION C1
7.00-8.00: Dinner/Breakfast | Midnight sun
04
Lighting
Filtered window contribution:
250-400 lux, 5000-6500 K
Artificial circadian system:
  Base light, ambient lights
200-300 lux, 3000-3500 K
  direct light
300-500 lux, 2700-3000 K
Final perceived: 450-900 lux, 3500-5000 K
Control system
Motion sensor:
  Both walls folded
  Dining table unfolded
Smart watch:
  User A: regular heart rate
  User B: heart rate increases
Environmental data: Midnight sun
Light
Brightness
Warmth
Rendered with Gemini
Notes: three configurations for showing our main variables:
- arctic summer not shaded
- arctic summer shaded (evening)
- arctic winter
- collective
- private
- semiprivate
(all of the lights)
Lighting
Filtered window contribution:
250-400 lux, 5000-6500 K
Artificial circadian system:
Base light, ambient lights
200-300 lux, 3000-3500 K
direct light
300-500 lux, 2700-3000 K
Final perceived: 450-700 lux, 4000-5000 K
Control system
Motion sensor:
Both walls folded
Dining table unfolded
Smart watch:
User A: regular heart rate
User B: high heart rate
Environmental data: Midnight sun

## Slide 30
04
7.00-8.00: Dinner/Breakfast | Midnight sun
Lighting
Filtered window contribution:
250-400 lux, 5000-6500 K
Artificial circadian system:
  Base light, ambient lights
200-300 lux, 3000-3500 K
  direct light
300-500 lux, 2700-3000 K
Final perceived: 450-900 lux, 3500-5000 K
Control system
Motion sensor:
  Both walls folded
  Dining table unfolded
Smart watch:
  User A: regular heart rate
  User B: heart rate increases
Environmental data: Midnight sun
SYSTEMS INTEGRATION | CONFIGURATION C1
Light
Brightness
Warmth
Heart rate adjustment
Rendered with Gemini
Notes: three configurations for showing our main variables:
- arctic summer not shaded
- arctic summer shaded (evening)
- arctic winter
- collective
- private
- semiprivate
(all of the lights)

## Slide 31
05.00-07.00: Leisure/Sleep | Midnight sun
Rendered with Gemini
04
Lighting
Filtered window contribution:
10-40 lux, 5500-6500 K (Selective shading)
(User A) Artificial circadian system:
  Base lights, ambient lights
40-150 lux, 1700-2000 K
  Direct light 150-300 lux, 2700-3500 K
Final perceived: 50-200 lux, 2000-3200 K
(User B) Artificial circadian system: 0 lux, 0 K
Final perceived: 0-20 lux, 8500-10000 K
Control system
Motion sensor:
  Wall user A folded
  Bed user B unfolded
Smart watch:
  User A: low heart rate
  UserB: very low heart rate
Environmental data: Midnight Sun, shaded
SYSTEMS INTEGRATION | CONFIGURATION C2
Light
Brightness
Warmth
Notes: Lighting
Filtered window contribution: 150-300 lux and 5000-65000 K
Artificial circadian system:
- Base light, ambient lights, direct
illuminance: 200-350 lux
colour: 3500-4500 K
Navigation light:
illuminance: 3-10 lux
color: 1800-200 K
Final perceived:
illuminance: 350-650 lux
colour: 5500-6400 K
Controls | Rest & Recovery:
Motion sensor:
Both walls unfolded
Beds unfolded
Smart watch:
Person A: low heart rate
Person B: very low heart rate
Environmental data:
Midnight sun, but shaded

## Slide 32
05.00-07.00: Leisure/Sleep | Midnight sun
04
Rendered with Gemini
Lighting
Filtered window contribution:
10-40 lux, 5500-6500 K (Selective shading)
(User A) Artificial circadian system:
  Base lights, ambient lights
40-150 lux, 1700-2000 K
  Direct light 150-300 lux, 2700-3500 K
Final perceived: 50-200 lux, 2000-3200 K
(User B) Artificial circadian system: 0 lux, 0 K
Final perceived: 0-20 lux, 8500-10000 K
Control system
Motion sensor:
  Wall user A folded
  Bed user B unfolded
Smart watch:
  User A: low heart rate
  UserB: very low heart rate
Environmental data: Midnight Sun, shaded
SYSTEMS INTEGRATION | CONFIGURATION C1
Personal preference
Warmth

## Slide 33
2700-4000 K
100-300 lux
2700-4000 K
100-300 lux
04
14.00-17.00: Sleep/work | Polar night
Lighting
Filtered window contribution:
0-20 lux, 8500-10000 K
(User A) Artificial circadian system:
  Navigation lights 3-10 lux, 1700-2000 K
Final perceived: 3-30 lux, 1700-2000 K
(User B) Artificial circadian system:
  Base light, ambient lights
600-750 lux, 5500-6500 K
  Direct light 500-650 lux, 4000-5000 K
Final perceived: 600-770 lux, 5500-6500 K
Control system
Motion sensor:
  Both walls unfolded
  Bed user A & desk user B unfolded
  User A out of bed
Smart watch:
  User A: low heart rate
  UserB: high heart rate (stress)
Environmental data: Polar night
SYSTEMS INTEGRATION | CONFIGURATION C3
Rendered with Gemini
Light
Brightness
Warmth

## Slide 34
2700-4000 K
100-300 lux
2700-4000 K
100-300 lux
04
14.00-17.00: Sleep/work | Polar night
Lighting
Filtered window contribution:
0-20 lux, 8500-10000 K
(User A) Artificial circadian system:
  Navigation lights 3-10 lux, 1700-2000 K
Final perceived: 3-30 lux, 1700-2000 K
(User B) Artificial circadian system:
  Base light, ambient lights
600-750 lux, 5500-6500 K
  Direct light 500-650 lux, 4000-5000 K
Final perceived: 600-770 lux, 5500-6500 K
Control system
Motion sensor:
  Both walls unfolded
  Bed user A & desk user B unfolded
  User A out of bed
Smart watch:
  User A: low heart rate
  UserB: high heart rate (stress)
Environmental data: Polar night
SYSTEMS INTEGRATION | CONFIGURATION C3
Rendered with Gemini
Light
Brightness
Warmth
Corrective fading

## Slide 35
Rendered with Gemini

## Slide 36
DIGITAL PROTOTYPE | LIGHTING
Arduino code
Jupyter code
Arduino UNO
Serial via
USB
12V
Power supply
+ GND
Warm white LED lights
&
Cool white LED lights
Gate
Source
Drain
+ calculate warm_pwm and cold_pwm
05
MOSFET 1
Warm channel
MOSFET 2
Cool channel
&
Arduino prototype setup

## Slide 37
  3D printed automated rotating mecanism
  attached to the table base and to the shelf edge
  wires integrated in the thickness of the table panel and shelf lower surface
Metal axle
Shelf fixed hinge housing
Table panel fixed hinge housing
05
DIGITAL PROTOTYPE | FRAGMENT LOGIC
Selected fragment
Rotating table panel
Notes: Goal: Show intelligence of assembly
Content:
Exploded axonometric of the fragment
detachable parts
Add labels:
automatically movable

## Slide 38
To control the mechanism
High-torque servo motor (MG996R type)
  Direct angle control (0–180°) → perfect for your table
  Compact (40mm x 19mm x 43mm)
  → easy to hide in the Voronoi structure
05
DIGITAL PROTOTYPE | FRAGMENT LOGIC
Arduino microcontroller
Wire integrated along structural ribs
Notes: Goal: Show intelligence of assembly
Content:
Exploded axonometric of the fragment
detachable parts
Add labels:
automatically movable

## Slide 39
Mesh with load from Karamba
(for the table panel)
Selection of a single panel
Stress curves
(red:compression, blue: tension)
Voronoi ribs structure from the stress curves
DIGITAL PROTOTYPE | STRUCTURAL OPTIMISATION
05

## Slide 40
Prototype geometry
Hinge connection
Production Method
RECYCLED PLASTIC
METAL
Additive D2RP
Material
05
Robotically 2D printed components
Demountable and
reconfigurable elements
Complex Voronoi
geometries
Repair
Replacement
Adaptation
Printed from recycled PET bottles
filament
Lightweight, durable, and suitable for modular furniture components
color: off white with small multicolor speckles: not to harsch, but clean, neutral and calm
reliable rotation and strength
precise inserted technical parts that complement printed geometry
DIGITAL PROTOTYPE | MATERIAL
Notes: Recycled PET
Goal: Show material thinking (not generic sustainability talk)
Content:
Close-up render or photo of of texture
Small diagram:
PET bottles → filament → printed element
Text
lightweight
durable
circular lifecycle
material reduction through geometry (very important concept)

## Slide 41
Thank you for your attention !